## Slide 1: QUIC: A UDP-Based Multiplexed and Secure Transport
Design, security, scalability, and a Wireshark demo
SIT202, Computer Networks and Communication
Hirusha Adikari / 225555137

## Slide 2: Why do we need QUIC?
1 Slow setup
TCP plus TLS costs 2 round trips before any data moves
2 Head of line blocking
One lost packet stalls every multiplexed request
3 Breaks on IP change
Switching networks kills every TCP connection
4 Can't evolve
Middleboxes assume TCP never changes
Chart: Round trips before first byte
| TCP + TLS 1.2 | TCP + TLS 1.3 | QUIC first connection | QUIC resumed (0-RTT)
Round trips (RTT) | 3 | 2 | 1 | 0

## Slide 3: What is QUIC?
Standardised by the IETF as RFC 9000 in 2021. It runs on UDP and lives inside the application instead of the OS.
Traditional HTTPS
QUIC (HTTP/3)
HTTP/2
TLS 1.3
TCP
IP
HTTP/3
QUIC (TLS 1.3 built in)
UDP
IP
User space
Ships with the app, so it updates fast.
Connection ID
Not tied to IP and port, so it survives network changes.
Always encrypted
Encryption is mandatory, not optional.

## Slide 4: Packets and frames
Long header
Used only during setup
Header form = 1
Packet type: Initial, 0-RTT, Handshake, Retry
Version
Destination Connection ID
Source Connection ID
Encrypted payload
Short header
Used after the handshake
Header form = 0
Destination Connection ID
Encrypted packet number
Protected payload
No version, no source ID, no length field
A datagram holds packets, and packets hold frames. Frames carry the control logic that TCP puts in header flags, but they sit inside the encrypted part.

## Slide 5: Key frame types
Frame type | What it does
CRYPTO | Carries the TLS handshake data
STREAM | Carries application data
ACK | Acknowledges received packets
PADDING | Fills packets to the required minimum size
MAX_DATA / MAX_STREAM_DATA | Flow control
NEW_CONNECTION_ID | Supplies spare IDs for migration
PATH_CHALLENGE / PATH_RESPONSE | Validates a new network path
HANDSHAKE_DONE | Server confirms setup is finished

## Slide 6: Cryptographic mechanisms
RFC 9001. TLS 1.3 is built into the handshake instead of layered on top.
Key exchange
TLS 1.3 handshake carried in CRYPTO frames
Authentication
Server X.509 certificate, same as HTTPS
Confidentiality
Every packet AEAD encrypted, AES-GCM or ChaCha20
Integrity
16 byte auth tag detects any tampering
Header protection
A second layer hides the packet number
Forward secrecy
Ephemeral keys, rotated during the connection
Why Wireshark can still read the start of a QUIC connection
Initial packets use keys derived from the Connection ID, so they are encrypted but not secret. That is why Wireshark can show the ClientHello with no key file at all.

## Slide 7: Threats and mitigations
Threat | What happens | Mitigation
0-RTT replay | Captured early data can be resent | Only allow safe, repeatable requests in 0-RTT
Amplification attack | Spoofed IP triggers an oversized reply | 3x response cap plus 1200 byte padded Initials
Handshake flooding | Many fake requests burn server CPU | Retry tokens validate the address first
UDP flooding | Raw volume attack on port 443 | QUIC aware DDoS scrubbing
User tracking | Reusing a Connection ID links two IPs | Fresh Connection ID on migration
Implementation bugs | Design is sound but a given library may not be | Fuzzing, patching, interop testing

## Slide 8: Live demo: Wireshark, QUIC vs TCP plus TLS
Capturing a live handshake, decrypting HTTP/3 with a TLS key log, and comparing round trips against a TCP capture.
1
No 3-way handshake
2
Read the ClientHello
3
Short header is opaque
4
Decrypt HTTP/3

## Slide 9: Applications of QUIC
HTTP/3
The web. No head of line blocking, faster setup.
DNS over QUIC
RFC 9250. Encrypted DNS that is still fast, with spoofing protection.
SMB over QUIC
Windows file shares over the internet, no VPN needed.
WebTransport
Modern replacement for WebSockets in the browser.
MASQUE
VPN style tunnels. Used by iCloud Private Relay and Cloudflare WARP.
Video platforms
YouTube, Instagram, Facebook. Fewer rebuffer stalls.
Don't assume every QUIC flow is HTTP/3. A lot of things share UDP 443 now.

## Slide 10: Scalability
Per connection
Where QUIC wins
Many streams on one connection
Two level flow control
One handshake replaces six TCP connections
Per server
This is the weak point
Higher CPU per packet
Every packet is encrypted on its own
Fixed with batching and UDP offload (GSO)
Infrastructure
Where it stays flexible
Load balancers route on Connection ID
Routing survives client IP changes
Fixes ship as a software release, not an OS update
One handshake, many streams. The cost moves off the network and onto the server CPU.

## Slide 11: QUIC vs TCP, captured evidence
Metric | TCP + TLS 1.3 | QUIC
Packets before first app data | [my capture] | [my capture]
Round trips before first data | 2 | 1 (0 if resumed)
Time to first byte | [measure] | [measure]
Header visible on the wire | Fully visible | About 1 byte plus Connection ID
Connection close visible | FIN/RST in cleartext | Encrypted frame
I fill the bracketed values in from my own Wireshark capture just before recording.

## Slide 12: Wrap up
1
QUIC isn't a faster TCP. It merges the transport and security handshakes into one.
2
Its biggest strength is also its biggest cost. Encrypting the header buys security but loses network visibility.
3
Most real QUIC risk comes from deployment gaps and library bugs, not the underlying cryptography.
References
[1] J. Iyengar and M. Thomson, Eds., "QUIC: A UDP-based multiplexed and secure transport," RFC 9000, IETF, May 2021.
[2] M. Thomson and S. Turner, Eds., "Using TLS to secure QUIC," RFC 9001, IETF, May 2021.
[3] A. Langley et al., "The QUIC transport protocol: Design and Internet-scale deployment," in Proc. ACM SIGCOMM, 2017, pp. 183 to 196.
[4] M. Kuhlewind and B. Trammell, "Manageability of the QUIC transport protocol," RFC 9312, IETF, Sep. 2022.
[5] E. Chatzoglou et al., "Revisiting QUIC attacks: A comprehensive review on QUIC security and a hands-on study," Int. J. Inf. Secur., vol. 22, no. 2, pp. 347 to 365, 2023.
[6] W3Techs, "Usage statistics of HTTP/3 for websites," 2026. Available: w3techs.com